Arduino Drum Sequencer
Samuel Thibodeau

---
Motivation
- Hardware interfacing
  - Immediacy
- Automation and control
- Arduino and Max based
- Performance options

---
Outline
- 16 steps with LEDs
- Multiple instruments, full drum kit
- Tempo knob
- Kit changing
- MIDI output

---
Limitations
- 18 usable pins
  - One per LED, button, or potentiometer
- 16 steps, limited buttons and LEDs

---
Arduino Wiring
- 8 LEDs
- 1 Step group shift
- 4 Step buttons
- Pause/Play/Reset
- Instrument Change
- Kit Change
- BPM control

---
Arduino Code
- Step data in binary array per instrument
- Instrument and step group flag
- LED output based on the above
- Loop continuously check pin status and then updates various flags

---
Instrument Map
- 4 = Open Hi-Hat
- 5 = Toms*
- 6 = Cymbal*
- 7 = Cowbell
- 8 = Roller
5 = Toms (Mid)
6 = Cymbal
7 = Cowbell
8 = Roller
- 0 = Kick*
- 1 = Snare*
- 2 = Clap
- 3 = Closed Hi-Hat

---
Button Pressing
- Instant toggling on detection of a HIGH pin → trouble
- Button pressing semaphore
- Detection of first press and release
  - Allows for separate press and hold functionality

---
Basic Flow (Button Pressing)
- First cycle where a button is pressed
  - Set the “pressed” flag to true and register which button is pressed in an array of 20 bits (one per pin)
  - Perform action of the button (case by case basis)
- Next iteration of CheckPress
  - Check if a button is pressed
    - If yes, check whether the currently pressed button is the one we are checking
      - If it is, check the pin state
        - If the pin is no longer HIGH, release the flags
        - Else do nothing
      - If it’s not, do nothing

---
Addendum
- Pressed flag is redundant
  - Currently prevents multiple button pressings
- Could be removed to allow button combination
  - Further functionality?

---
Max Patch
- Receive Arduino messages
- Parse based on the first byte
- Nested design, with instrument, timing, and io modules

---
Interesting Features
- Roller
- Pause / Play / Reset and Instrument sound toggle
- Arduino speed

---
Wish-list
- LEDs flashing in time with the steps being played
- Photoresistor sensor to manually play instruments
- Physical feedback for instrument and step group